## Slide 1: ERASURE CODING HW ACCELERATOR
project mid-semester presentation
Or Dadush
Nadav Zaharia

## Slide 2: Booming of Data
The booming of data makes storage overhead of replication considerable
Notes: הקדמה על גדילת המידע והיחלשות חוק מור
הגדרת הפרוייקט ואיך הגענו לEC

## Slide 3: Fault Tolerance & Replication
Fault tolerance is a critical requirement for distributed storages
  Availability
  Durability
Erasure coding:
  Takes in k data chunks and generates m parity chunks
  Distributes (k + m) chunks to (k + m) independent nodes
Notes:   זמינות – המידע עדיין זמין לאחר נפילות
  עמידות – המידע בר שחזור לאחר נפילות
  פתרון טריוויאלי – שכפול X3
  RAID 6\5
  4. EC – גמישה -> יעילות והתאמה לכל מקרה (מערכת אחסון)
  Availability: data is still accessible under failures
  Durability: no data corruptions under failures
  data is stored in physical devices
  the devices fail randomly hence fault tolerance is needed
  EC is efficient in storage overhead but inefficient computation wise.
  K is the granularity of restoration
  M gives tradeoff between availability and storage overhead (bc we can lose M shards simu)

## Slide 4: Definition and Goals
Design and implement a generic hardware accelerator for efficient encoding of data blocks using erasure coding.
Goals:
- Maximal genericity
- cpu offloading
- Compatibility to existing solutions.
- Power consumption.
- Minimal on-chip memory.
- Area efficiency
- Real time performance.

## Slide 5: Cauchy Reed-Solomon Codes
matrix multiplication on finite Galois field
Notes: we want to have an equation so that a reversable matrix ties between the original k shards and the k+m shards.
the matrix should be reversable for every set of remaining shards between K + M -1 to K shards
the solution is Cauchy matrix that is reversable for every submatrix of itself
the mult and addition is on GF
matrix mult is computational heavy but highly parallel

## Slide 6: Alternative solutions:
alternative solutions:
  software: Jerasure, Intel ISA-L, Gibraltar (gpu)
  NIC: Mellanox-EC
  FPGA: SoftIron, Academic paper. (*)
alternative implementations:
  No known generic EC implementations in ASIC
  GF operations using LUT
(*) Mian Qin, et al “A Generic FPGA Accelerator for Minimum Storage Regenerating Codes”
Notes: hardware alternatives – FPGA is generic by default. LUT is available

## Slide 7: Fast GF Ops – Binary Representation
Notes: explanation on the method
  turn the matrix numbers to W x W bitmatrix
  turn the data numbers to W bits vector
  mult just like a regular matrix mult but in W = 1
  why this over LUT:
  AREA – each look up table will be 2^W and we’ll need
  easy to implement in ASIC -> simple control and design
  3. POWER

## Slide 8: Architecture - overview
CPU only involved in setup and data transmission
Notes: CPU only sends data and where to store once to the acc - > offloading
we focused on the engine and not the IF as Bnya instructed

## Slide 9: Architecture – Block Diagram
Notes: ASK BNYA if to drop this

## Slide 10: Micro-Architecture
Notes: explain data movement – only read once

## Slide 11: Micro-Architecture - Engine
Main parameters:
  K - a coded data block is divided to k shards.
  M - number of redundant produced shards.
  K_TAG – number of basic processing units.
  K_min
  K_max
  Packet = W * packet_length
Notes: and+xor units – they do the w^2 bitmatrix product
dyn xor does the xor between the bitmatrixes products
ASK BNYA – how much should we talk about micro ARCH of genericty (dyn xor ect)
explain k min/max and packet parameters and how they effect

## Slide 12: Fast GF Ops – Binary Representation
Notes: explanation on the method
  turn the matrix numbers to W x W bitmatrix
  turn the data numbers to W bits vector
  mult just like a regular matrix mult but in W = 1
  why this over LUT:
  AREA – each look up table will be 2^W and we’ll need
  easy to implement in ASIC -> simple control and design
  3. POWER

## Slide 13: Status
So far:
  survey of computation-heavy challenges in the distributed data storage area.
  Examination of a wide range of erasure coding solutions and implementations.
  Architectural and micro-architectural design
  Software simulator implementation
To be done:
  RTL implementation and verification
  Performance analyze
  Synthesis + Layout

## Slide 14: Schedule
Gantt Chart:
stage\week | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Exploring problems in data storage area |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Erasure Coding solutions examination |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Architectural and micro-architectural design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Software Simulation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RTL Implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Functional simulation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Synthesis |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Layout Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |